PENGARUH BENTUK (POWDER, GRANULE, DAN GRAVEL) KARBON AKTIF DARI BAMBU TERHADAP DEBIT DAN EFISIENSI ABSORBSI PADA PENJERNIHAN AIR SELOKAN MATARAM

Oleh:

Aldian Nindya

NIM 11306144039

ABSTRAK

Penelitian ini bertujuan untuk mengetahui pengaruh bentuk (powder, granule, dan gravel) karbon aktif dari bambu terhadap efisiensi absorbsi karbon aktif dengan indikator efisiensi transmisi cahaya pada sampel air Selokan Mataram, serta lamanya waktu kontak (contact time) yang dibutuhkan atau besar kecilnya debit sebagai indikator lamanya proses penjernihan sampel air selokan mataram.

Subjek penelitian ini adalah karbon aktif dari bambu dalam ukuran powder (100 mesh / 0,149 mm), granule (8 mesh / 2,4 mm) dan gravel (4 mesh / 4,76 mm). Objek penelitian ini adalah air Selokan Mataram hasil penyaringan menggunakan karbon aktif dalam bentuk powder, granule, dan gravel dengan variasi massa. Air Selokan Mataram dilewatkan pada kolom penukar ion yang di dalamnya terdapat karbon aktif. Selama proses penjernihan dicatat lamanya waktu yang dibutuhkan. Air Selokan Mataram yang telah diberikan perlakuan diukur efisiensi transmisi cahayanya sebagai indikator kejernihan. Hasilnya dianalisis menggunakan persamaan debit dan efisiensi.

Hasil penelitian menunjukkan bahwa karbon aktif dari bambu dalam bentuk granule memiliki tingkat efisiensi absorbsi yang terbaik dibandingkan dengan karbon aktif dalam bentuk powder dan gravel. Efisiensi absorbsi dari air Selokan Mataram hasil penyaringan menggunakan karbon aktif berbentuk granule mencapai (94 ± 2)% saat massa karbon aktif 37 gram. Hasil penelitian juga menunjukkan bahwa waktu kontak (contac time) meningkat atau debit bertambah kecil seiring bertambah kecil bentuk karbon aktif yang digunakan.

Kata kunci: karbon aktif dari bambu, absorbsi, powder, granule, gravel, debit, efisiensi absorbsi, air selokan mataram

THE INFLUENCE OF FORM (POWDER, GRANULE AND GRAVEL) ACTIVATED CARBON FROM BAMBOO TO RATE OF FLOW OF WATER AND ABSORBTION EFFICIENCY IN WATER PURIFICATION SELOKAN MATARAM

By :

Aldian Nindya

NIM 11306144039

ABSTRACT

This study aims to determine the effect of form (powder, granule and gravel) activated carbon from bamboo to efficiency of activated carbon absorbtion with indicator light transmission efficiency at sample Selokan Mataram water, and the duration of contact time required or major or minor rate of flow of water as indicator duration of the process of purification of water sample Selokan Mataram.

The subject of this study is activated carbon from bamboo in size powder (100 mesh/0,149 mm), garanule (8 mesh/2,4 mm) and gravel (4 mesh/4,76 mm). The object of this study is result Selokan Mataram water purification process using activated carbon in the form powder, granule and gravel with mass variation. Selokan Mataram water is passed to the ion exchange column in wich there is activated carbon. During purification process recorded duration time needed.  Selokan Mataram water has been given treatment measured light transmission eficiency as indicator of pureness. The result were analyzed using rate of flow of water and efficiency equation.

The result of study indicate that activated carbon from bamboo in form of granule have the best absorbtion efficiency levels compared to activated carbon in the form of powder and gravel. Absorbtion efficiency from Selokan Mataram water of purification result using the activated carbon in the form granule reached (94 ±2 )% when the activated carbon mass 37 grams. The result also indicate that increased contact time or  rate of flow of water a small increase due to incraese small form activated carbon used.

keyword: activated carbon from bamboo, absorbsi, powder, granule, gravel, absorbtion efficiency, rate of flow of water